## Slide 1
CPS: Medium: Integrated Design of Sensing, Network, and Cooperative Control of Multi-Vehicle Systems for Preventing Frost and Freeze Damage to Flowers and Buds of Fruit Trees
David James Lyons PhD
Autonomy Perception and Cognition Department
Summer 2019

## Slide 2
Platform(s) Communication
Spatial Data Manager Suite
Decision Space Analysis
UGV Heating system
Preliminary Study

## Slide 3
BASE
STN.
UAV
FLIR camera
∆T (leaving - arrival)
Battery level
grid (x,y) position
boolean activation of dragon
Flight path (way points)
FLIR grid (x,y) position
FAH
FLIR images
battery level
Communication Overview
DJI
Flight
Controller
ODROID
DJI
Remote
Communication Key
Wi-Fi
Serial (USB to TTL)
RF
Flight commands
UGV
ODROID
Driving commands
Husky Motor
Controller
Safeguard Default Interrupt

## Slide 4: ROS File Schema
In ROS filesystems a hierarchy must be applied in order to allow for consistent and trouble-free launches when running the full system network for the base station and UAV/UGV. The format is created within the dji_sdk package as a centralized location and each subsection lies within its relevant folder. Multiple mid-level launch files and low-level nodes will exist and called using the master launch file. The overall format is as follows, each point represents an individual file:
Launch master file (using <include>)- xml
  Launch file(s)- xml
    Node(s) (publisher/subscriber/client/server)- Python

## Slide 5: ROS File Syntax
ROS does not specifically require a file name hierarchy or syntax thus one was created for the project in order to maintain consistency. In order to differentiate nodes and launch files based on their responsibilities, a suffix-based syntax will be maintained among all ROS files and scripts. The rules are as follows:
All top and mid-level launch files will be specific to the vehicle they operate. Ending in “_uav” or “_ugv” (ex. “gui_launch_uav.launch”)
Publisher/subscriber (topic) nodes will end in “_sub” or “_pub”. (ex. “battery_state_sub”)
Client/server (service) nodes will end in “_cli” or “_serv”. (ex. “mission_waypoint_upload_cli”)
*No capital letters will be used in any filename. Exceptions to the above syntax will be made for dji_sdk based nodes to minimize issues with addressing filenames in pre-written scripts and launch files. NOTE: All python based node scripts also require “.py”

## Slide 6: ROS UAV Framework
Dji_sdk package
UDP
(Pub/Sub)
TCP/IP
(client/server)
GUI
Base Station
Onboard Odroid
Battery_sub
Flight
_status_sub
Height
_above
_takeoff_sub
Velocity_sub
Mission Flight Control
Mission_waypoint_upload_cli
Mission_waypoint_action_cli
GUI
Battery_pub
Flight
_status_pub
Height
_above
_takeoff_pub
Velocity_pub
Mission Flight Control
Mission_waypoint_upload_serv
Mission_waypoint_action_serv
Publisher/Subscriber Communication
Client/Server Communication
Node
Key

## Slide 7: Temperature Monitoring Agent
UAS+FLIR
Temp. Monitor Agent:
Interpret cooling rate for flagged areas
Create path plan for UGV to heat areas
UGV
GPS path plan
GPS-based temperature values
GPS coordinates of flagged areas
INPUT DATA
OUTPUT DATA

## Slide 8: Spatial Data Manager (SDM) Parameters
Gimbal Field of View (FOV)
Gimbal Angle (Θ)
Θ
UAS Height (AGL)

## Slide 9
GPS: Standard deviation 1.25 [m]
Target width 0.6 [m]
Target length 1.21 [m]
Row spacing 3.0 [m]
*all numbers are approximate
GPS and Target size are the same order of magnitude.

## Slide 10: Field Coordinate Transform (Global to Fixed Region)- Block A1 Example
Global Coordinate System (X,Y)
Fixed Region Coordinates (x,y)
Reference trees
Θ
Y (North)
X (East)
dx
dy

## Slide 11
Encoding of GPS latitude & longitudinal positions to a spatial grid map used for reasoning in the decision space.

## Slide 12: Ground Station Decision Tree
  Ambient temperature below Tcrit?
    Begin path planning
      R value variance of last flight pictures compared to baseline images
      Battery life >15%?
        Return error value
      Grid areas previously/soon to be heated by UGV
        Deploy drone
    Repeat ambient temperature reading
  Thermistor sensor reading
  Deploy initialization stage
  Path planning
  considered variables
  Deploy decision

## Slide 14: Preliminary Study for EMF exposure
Healthy Flower
  Magnified at 63x
  Average cell size is ~30 micrometer
  Cell Count ~60
Baseline image of a healthy cell.

## Slide 15
I. Frozen Flower at -20°C
Five minutes at -20°C
Ten minutes at -20°C
Fifteen minutes at -20°C
Baseline

## Slide 16
II. Heated Blossoms
Three seconds
Five seconds
Baseline
Ten seconds

## Slide 17
III. Heated Blossoms
Fifteen seconds
Baseline
Twenty seconds
Time [seconds] | Cell Size [micrometers] | Cell Count
3 | 70-80 | 20
5 | 50-70 | 25
10 | 50-60 | 40
15 | 50-60 | 30
20 | 45-50 | 50

## Slide 18: END